## Slide 1: 19CSE301 COMPUTER NETWORKS 3-0-3 4

## Slide 2
APPLICATION LAYER
Peer to Peer Applications

## Slide 3: Pure P2P architecture
no always-on server
arbitrary end systems directly communicate
pairs of intermittently connected hosts, called peers, communicate directly with each other.
examples:
  file distribution (BitTorrent)
  Streaming (KanKan)
  VoIP (Skype)
Application Layer
2-24

## Slide 4: P2P File distribution
We begin our foray into P2P by considering a very natural application, namely,
distributing a large file from a single server to a large number of hosts (called peers).
In client-server file distribution, the server must send a copy of the file to each of the peers—placing an enormous burden on the server and consuming a large amount of server bandwidth
In P2P file distribution, each peer can redistribute any portion of the file it has received to any other peers, thereby assisting the server in the distribution process.

## Slide 5: File distribution: client-server vs P2P
Question: how much time to distribute file (size F) from one server to
N peers?
peer upload/download capacity is limited resource
Application Layer
2-26
us
uN
dN
server
network (with abundant
bandwidth)
file, size F
us: server upload capacity
ui: peer i upload capacity
di: peer i download
capacity
u2
d2
u1
d
1
di
ui

## Slide 6: Distribution time for the client- server architecture
To determine the distribution time for the client-server
architecture- Dcs
The server and the peers are connected to the Internet with access links. Denote the upload rate of the server’s access link by us, the upload rate of the ith peer’s access link by ui, and the download rate of the ith peer’s access link by di. Also denote the size of the file to be distributed (in bits) by F and the number of
peers that want to obtain a copy of the file by N.
An illustrative file distribution
problem
The distribution time is the time it takes to get a copy of the file to all N peers.
The distribution time increases linearly with the number of
peers N.

## Slide 7: File distribution time: client-server
server transmission: must sequentially send (upload) N file copies:
time to send one copy: F/us
time to send N copies: NF/u
s
Application Layer
2-28
increases linearly in N
time to distribute F to N clients using client-server approach
Dc-s > max{NF/us,,F/dmin}
client: each client must download file copy
  dmin = min client download rate
  min client download time: F/dmin

## Slide 8
File distribution time: P2P
Scalability of P2P Architectures

## Slide 9: File distribution time: P2P
server transmission: must upload at least one copy
time to send one copy: F/us
Application Layer
2-30
time to distribute F to N clients using P2P approach
us
network
di
u
i
F
DP2P > max{F/us,,F/dmin,,NF/(us + ui)}
client: each client must download file copy
  min client download time: F/dmin
clients: as aggregate must download NF bits
  max upload rate (limiting max download rate) is us + ui
increases linearly in N …
… but so does this, as each peer brings service capacity

## Slide 10: Client-server vs. P2P: example
Application Layer
2-31
2.5
2
1.5
1
0.5
0
3
0
5
10
15
20
25
30
35
N
Minimum Distribution Time
P2P
Client-Server
client upload rate = u, F/u = 1 hour, us = 10u, dmin ≥ us
3.5

## Slide 11: P2P file distribution: BitTorrent
Application Layer
tracker: tracks peers
participating in torrent: When a peer joins a torrent, it registers itself with the tracker and periodically
informs the tracker that it is still in the torrent
file divided into 256Kb chunks
peers in torrent send/receive file chunks
Alice arrives …
… obtains list
of peers from tracker
… and begins exchanging
file chunks with peers in torrent
The collection of all peers participating in the distribution of a particular
file is called a torrent
Once a peer has acquired the entire file, it may (selfishly) leave the torrent, or (altruistically) remain
in the torrent and continue to uploa
chunks to other peers. Also, any peer
may leave the torrent at any time with only a subset of chunks, and later rejoin the torrent
2-32

## Slide 12: P2P file distribution: BitTorrent
peer joining torrent:
  has no chunks, but will accumulate them over time from other peers
  registers with tracker to get list of peers, connects to subset of peers (“neighbors”)
    while downloading, peer uploads chunks to other peers
    peer may change peers with whom it exchanges chunks
    churn: peers may come and go
    once peer has entire file, it may (selfishly) leave or (altruistically) remain in torrent
Application Layer
2-33

## Slide 13: BitTorrent: requesting, sending file chunks
requesting chunks:
at any given time, different peers have different subsets of file chunks
periodically, Alice asks each peer for list of chunks that they have
Alice requests missing chunks from peers, rarest first
Application Layer
2-34
sending chunks: tit-for-tat
Alice sends chunks to those four peers currently sending her chunks at highest rate
  other peers are choked by Alice
(do not receive chunks from her)
re-evaluate top 4 every10 secs
every 30 secs: randomly select another peer, starts sending
chunks
“optimistically unchoke” this peer
newly chosen peer may join top 4
So at any given instant of time, Alice will have a subset of chunks and will know which chunks her neighbors have.
With this information, Alice will have two important decisions to make.
First, which chunks should she request first from her neighbors?
And second, to which of her neighbors should she send requested chunks?

## Slide 14: BitTorrent: tit-for-tat
Application Layer
2-35
Alice “optimistically unchokes” Bob
Alice becomes one of Bob’s top-four providers; Bob reciprocates
Bob becomes one of Alice’s top-four providers
higher upload rate: find better
trading partners, get file faster !